## Slide 1: Machine Learning Strategies for Chemistry Tabulation and Lookup
Amol Salunkhe, Siddhant Aphale, Paul Desjardin and Varun Chandola

## Slide 2: Turbulent Combustion Modeling
Numerical simulations of turbulent combustion problems is expensive
  Large number of molecular species present
  Large disparity between the scales for the flame (combustion) and the flow
A typical model reduction strategy is to project the high-dimensional thermochemical state-space on a low-dimensional manifold
  The state-space is precomputed and parameterized in terms of a reduced set of scalar variables (tabulation)
  The flow system is solved using the scalar variables (model reduction)
  The full state space (chemistry) is efficiently looked up during run-time
Advantage: decouple the turbulent flow field (exists at a coarser time/spatial scale) and the chemical reactions (exist at a much finer time/spatial scale)
Src: S. Bhalla et al., 2019, ECML-PKDD

## Slide 3: Reducing Chemistry
The thermochemical manifold is parameterized using:
  Conserved scalar (mixture fraction, Z)
  Reaction progress variables (e.g., Cpv in Bojko and Desjardin, 2016)
The reaction progress variable, C, can be calculated in several ways
  Intrinsic low dimensional manifold (ILDM – Mass and Pope, 1992)
  Flame Generation Manifolds (FGM)
Guiding principles for C
  C1 - Result in transport equation that can be conveniently solved
  C2 - The reactive scalars should evolve on comparable time scales
  C3 - Parameters should be independent of each other
  C4 - A bijective mapping from manifold space to the thermo-chemical state space

## Slide 4: Example of existing approaches
  Fixed expressions
  Data-driven calculations
  The weights are estimated by optimizing over a cost-function that imposes the monotonicity requirement (for C4)

## Slide 5: Run-time lookup
The mapping from lower-dimensional manifold parameterized by (Zmix, Cpv) to the state variables is pre-computed and tabulated
At run-time, for a new value of (Zmix, Cpv), a “look-up” is performed
  Lagrange interpolation

## Slide 6: Issues
The look-up could be computationally inefficient
In order to satisfy C4 (bijective mapping), several flames in the original data are removed before building the look-up table
  Inaccurate estimation of the thermochemical space
This could be improved by including more progress variables
  Would make interpolation even more inefficient
  Polynomial growth of the look-up table

## Slide 7: Proposed Machine Learning Based Framework 1
Step 1: Use principal component analysis (PCA) to learn the progress variables
  Linear combination of the species, so transport equation in the reduced space is convenient to solve (C1)
  Combines similarly evolving species (C2)
  Orthogonal basis vectors (C3)
    A constrained PCA formulation can be used to include Zmix
  However, it does not guarantee a smooth manifold over the state variables for efficient lookup (C4)
    Adding more PCA components would help
Step 2: Use a non-linear machine learning model to replace the tabular lookup
  A Gaussian Process Regression model
    Also provides uncertainties with the predictions
    Computationally inefficient
  A neural network
    Could be computationally inefficient

## Slide 8: Proposed Machine Learning Based Framework 1
High dimensional input vector
Low-dimensional state
ML predictive model
Thermochemical state variables
Run-time
Pre-computation
Constrained PCA

## Slide 9: Results so far
Tested constrained PCA + Gaussian Process Regression (GPR) on multiple scenarios (CH4 + Air, Wax + Air)
Evaluated on the predictive accuracy for the source energy term
Improvements over the current tabulated framework
  Especially when the low-dimensional state is increased to 5
Switching GPR for a neural network did not improve the results

## Slide 10: Proposed Machine Learning Based Framework 2
The reduction and the ML model lookup steps are decoupled in the first framework
  PCA focuses on maximizing the variance of the high-dimensional data in the low-dimensional reduction (C1, C2, C3)
  Is not necessarily informed by the subsequent task of predicting the high-dimensional state (C4)
The second framework combines the two steps into a coupled neural network architecture

## Slide 11: Proposed Machine Learning Based Framework 2
The first neural network is trained to accurately predict the target state variables (source energy, temperature, etc.) from the input high-dimensional input vector
The first layer has a linear activation and a bottleneck – width of the layer corresponds to the dimensionality of the reduced space
High dimensional input vector
Thermochemical state variables
PCA reduced representation
Neural network 1
Neural network 2
Linear layer

## Slide 12: Proposed Machine Learning Based Framework 2
The second neural network is trained to recover the PCA based reduction of the high-dimensional input
Both networks are jointly trained
High dimensional input vector
Thermochemical state variables
PCA reduced representation
Neural network 1
Neural network 2
Linear layer

## Slide 13: Proposed Machine Learning Based Framework 2
At run time, the reduced state from the flow computations are fed to the first neural network to estimate the thermochemical state
High dimensional input vector
Thermochemical state variables
PCA reduced representation
Neural network 1
Neural network 2
Linear layer
From the reduced order flow model

## Slide 14: Results
To be added soon!